Planning Act
Loi sur l’aménagement du territoire

ONTARIO REGULATION 784/21

ZONING ORDER - CITY OF BRAMPTON, REGIONAL MUNICIPALITY OF PEEL

Consolidation Period:  From November 24, 2021 to the e-Laws currency date.

No amendments.

This Regulation is made in English only.

Definition

1.  In this Order,

“Zoning By-law” means Zoning By-Law No. 270-2004 of the City of Brampton.

Application

2.  This Order applies to lands in the City of Brampton in the Regional Municipality of Peel, in the Province of Ontario, being the lands on a map numbered 282 and filed at the Toronto office of the Ministry of Municipal Affairs and Housing located at 777 Bay Street.

Urban Residential Zone

3.  (1)  This section applies to the lands located in the area shown as the Urban Residential Zone on the map referred to in section 2.

(2)  Every use of land and every erection, location or use of any building or structure is prohibited on the lands described in subsection (1), except for,

(a)	single detached dwellings;

(b)	townhouse dwellings;

(c)	rear lane townhouse dwellings;

(d)	back-to-back townhouse dwellings;

(e)	stacked townhouse dwellings;

(f)	apartment dwellings; and

(g)	a public park.

(3)  Despite the Zoning By-law, the following requirements apply to the uses, buildings and structures permitted under clause (2) (a):

1.	The minimum lot area is 325 square metres.

2.	The minimum lot frontage is 11.5 metres.

3.	The minimum lot depth is 28 metres.

4.	The minimum front yard setback is 6 metres to the garage and 4.5 metres to buildings or structures.

5.	The minimum exterior yard setback is three metres.

6.	The minimum interior side yard setback is 1.2 metres on one side and 0.6 metres on the other.

7.	The minimum rear yard setback is seven metres.

8.	The maximum building height is 11 metres.

9.	There is no maximum lot coverage.

10.	The minimum landscaped open space is 30 per cent of the minimum front yard area.

(4)  Despite the Zoning By-law, the following requirements apply to the uses, buildings and structures permitted under clauses (2) (b) and (c):

1.	The minimum lot area is 105 square metres per dwelling unit.

2.	The minimum lot frontage is 4.5 metres.

3.	There is no minimum lot depth.

4.	The minimum front yard setback is 6 metres to the garage and 4.5 metres to buildings or structures.

5.	The minimum exterior yard setback is three metres.

6.	There is no minimum interior side yard setback.

7.	The minimum rear yard setback is six metres.

8.	The maximum building height is 13.5 metres.

9.	There is no maximum lot coverage.

10.	The minimum landscaped open space is 30 per cent of the minimum front yard area.

11.	The minimum distance between buildings is 1.2 metres.

12.	Lot frontages may occur on a public or private lane.

(5)  Despite the Zoning By-law, the following requirements apply to the uses, buildings and structures permitted under clause (2) (d):

1.	The minimum lot area is 65 square metres per dwelling unit.

2.	The minimum lot frontage is 5.5 metres.

3.	The minimum lot depth is 24 metres.

4.	The minimum front yard setback is three metres.

5.	The minimum exterior yard setback is three metres.

6.	The minimum interior side yard setback is 0.6 metres.

7.	There is no minimum rear yard setback.

8.	The maximum building height is 13.5 metres.

9.	There is no maximum lot coverage.

10.	The minimum distance between buildings containing dwelling units is 2.4 metres.

11.	Lot frontages may occur on a public or private lane.

(6)  Despite the Zoning By-law, the following requirements apply to the uses, buildings and structures permitted under clause (2) (e):

1.	The minimum lot area is 90 square metres per dwelling unit.

2.	The minimum lot width is 30 metres.

3.	The minimum lot depth is 24 metres.

4.	The minimum front yard setback is three metres.

5.	The minimum exterior yard setback is three metres.

6.	The minimum interior side yard setback is 0.6 metres.

7.	The minimum rear yard setback is 6.0 metres.

8.	The maximum building height is 13.5 metres.

9.	There is no maximum lot coverage.

10.	The minimum distance between buildings or structures containing dwelling units is 2.4 metres.

11.	Lot frontages may occur on a public or private lane.

(7)  Despite the Zoning By-law, the following requirements apply to the uses, buildings and structures permitted under clause (2) (f):

1.	There is no minimum lot area.

2.	The minimum lot frontage is 30 metres.

3.	There is no minimum lot depth.

4.	The minimum front yard setback is six metres.

5.	The minimum exterior yard setback is six metres.

6.	The minimum interior side yard setback is six metres.

7.	The minimum rear yard setback is six metres.

8.	The maximum building height is 16 storeys.

9.	There is no maximum lot coverage.

10.	The minimum landscaped open space is 30 per cent.

(8)  Despite the Zoning By-law, the following requirements apply to the uses, buildings and structures permitted under clause (2) (g):

1.	The minimum front yard setback is three metres.

2.	The minimum exterior yard setback is three metres.

3.	The minimum interior side yard setback is three metres.

4.	The minimum rear yard setback is three metres.

(9)  The minimum density for the lands referred to in subsection (1) shall be 41 dwelling units per hectare.

Floodplain Zone

4.  (1)  This section applies to the lands located in the area shown as the Floodplain Zone on the map referred to in section 2.

(2)  Every use of land and every erection, location or use of any building or structure is prohibited on the lands described in subsection (1), except for,

(a)	flood and erosion control;

(b)	the protection, maintenance, enhancement and restoration of ecosystem forms and functions;

(c)	a public park;

(d)	a golf course; and

(e)	public uses, including stormwater management facilities and any associated structures.

Terms of use

5.  (1)  Every use of land and every erection, location and use of buildings or structures shall be in accordance with this Order.

(2)  Nothing in this Order prevents the use of any land, building or structure for any use prohibited by this Order if the land, building or structure is lawfully so used on the day this Order comes into force.

(3)  Nothing in this Order prevents the reconstruction of any building or structure that is damaged or destroyed by causes beyond the control of the owner if the dimensions of the original building or structure are not increased and its original use is not altered.

(4)  Nothing in this Order prevents the strengthening or restoration to a safe condition of any building or structure.

Deemed by-law

6.  This Order is deemed for all purposes, except the purposes of section 24 of the Act, to be and to always have been a by-law passed by the council of the City of Brampton.

7.  Omitted (provides for coming into force of provisions of this Regulation).

Back to top