Français

Rent Control Act, 1992

ONTARIO REGULATION 21/95

No Amendments

MAINTENANCE STANDARDS

Note:  This Regulation became spent some time before January 1, 2004.

This is the English version of a bilingual regulation.

PART 1
INTERPRETATION AND APPLICATION

1.  In this Regulation,

“appliances” include refrigerators, stoves, clothes washers, clothes dryers, dishwashers and hot water tanks;  (“appareils ménagers”)

“Building Code” means the building code under the Building Code Act, 1992;  (“Code du bâtiment”)

“exterior common areas” include roads, pathways, parking areas and garbage storage areas;  (“aires communes extérieures”)

“Fire Code” means the fire code under the Fire Marshals Act;  (“Code de prévention des incendies”)

“guard” means a barrier, that may or may not have openings through it, to prevent people from accidental falls; (“garde-corps”)

“habitable space” means a room or area used or intended to be used for living, sleeping, cooking or eating purposes and includes a washroom;  (“local habitable”)

“interior common areas” include laundry rooms, garbage rooms, corridors, boiler rooms, parking garages, storage areas and recreation rooms;  (“aires communes intérieures”)

“land lease community” means a residential complex containing rental units that are sites on which there are single-family dwellings that are permanent structures;  (“communauté de terrains à bail”)

“sewage system” means a municipal sanitary sewage system or a private sewage disposal system and includes a sewage system as defined in Part VIII of the Environmental Protection Act, and a sewage works as defined in the Ontario Water Resources Act;  (“système d’égouts”)

“washroom” means an area containing a toilet, urinal, bathtub, shower or washbasin.  (“salle de bains”)  O. Reg. 21/95, s. 1.

2.  (1)  This Regulation prescribes the maintenance standards for purposes of subsection 36 (1) of the Act.

(2)  The landlord shall ensure that the maintenance standards in this Regulation are complied with.  O. Reg. 21/95, s. 2.

3.  (1)  Subject to subsection (2), this Regulation applies to a residential complex and the rental units located in it if the residential complex is located in,

(a)	an area set out in the Schedule;

(b)	an area where a by-law under section 31 of the Planning Act or a predecessor of it or passed under any special Act respecting standards for maintenance and occupancy is in force but does not apply to the residential complex; or

(c)	an area where a by-law described in clause (b) is in force but that does not contain standards with respect to the interiors of the residential complex.

(2)  This Regulation does not apply to regulate standards for exteriors of a residential complex in an area where a by-law described in clause (1) (c) is in force.  O. Reg. 21/95, s. 3.

PART II
STRUCTURAL ELEMENTS

4.  The structural elements in a residential complex shall be maintained in a sound condition so as to be capable of safely sustaining their own weight and any load or force that may normally be imposed.  O. Reg. 21/95, s. 4.

5.  (1)  Every foundation wall, basement, cellar or crawl space floor, slab at ground level, exterior wall and roof shall be structurally sound, weathertight and damp-proofed and shall be maintained so as to reasonably protect against deterioration, including that due to weather, fungus, dry rot, rodents, vermin or insects.

(2)  Storm water run off shall be drained from the grounds of the residential complex and any area below exterior grade so as to prevent excessive ponding, erosion or the entrance of water into a building or structure.  O. Reg. 21/95, s. 5.

6.  (1)  Every roof shall be watertight.

(2)  The roof and any cornice flashing, fascia, soffit, coping, gutter, rainwater leader, vents or other roof structure,

(a)	shall be maintained to properly perform their intended function; and

(b)	shall be kept clear of obstructions, hazards and dangerous accumulations of snow and ice.  O. Reg. 21/95, s. 6.

7.  Retaining walls, guards and fences in exterior common areas shall be maintained in a structurally sound condition, free from hazards.  O. Reg. 21/95, s. 7.

8.  (1)  A landlord who disputes the need for repairs ordered under section 4, 5, 6 or 7 may submit a written report signed by a professional engineer licensed to practise in the relevant discipline in Ontario on the matters related to the ordered repairs.

(2)  If, in the opinion of the inspector, the report demonstrates that one or more of the repairs required by the order are not necessary in order to comply with this Regulation, the inspector shall, where it is appropriate, accept the report as evidence that the landlord has complied with one or more of the repairs required by the order.

(3)  If, in the opinion of the inspector, the report demonstrates that compliance with this Regulation may be obtained by a method other than that set out in the order, the inspector shall, where it is appropriate, amend the order.  O. Reg. 21/95, s. 8.

PART III
UTILITIES, SERVICES, ETC.

PLUMBING

9.  (1)  Plumbing and drainage systems and appurtenances in a residential complex shall be maintained free from leaks, defects or obstructions and adequately protected from freezing.

(2)  A residential complex shall be provided with a means of sewage disposal.

(3)  The means of sewage disposal shall be maintained in a good state of repair.  O. Reg. 21/95, s. 9.

10.  (1)  Subject to subsections (2) and (3), every rental unit shall contain the following fixtures:

1.	A toilet.

2.	A kitchen sink.

3.	A washbasin.

4.	A bathtub or shower.

(2)  Subsection (1) does not apply with respect to rental units that share a fixture described in paragraph 1, 2 or 4 of subsection (1) as long as no more than two rental units share the fixture and access to the fixture from each unit is possible without passing through,

(a)	another rental unit;

(b)	along an unheated corridor; or

(c)	outside the building containing the rental units.

(3)  Subsection (1) does not apply with respect to a boarding house or lodging house as long as there is at least one toilet, one washbasin and one bathtub or shower for every five rental units and all tenants shall have access to a kitchen sink.

(4)  The fixtures required by this section shall be maintained and shall be supplied with a supply of potable water sufficient for normal household use at a flow and pressure sufficient for the intended use of the fixtures.  O. Reg. 21/95, s. 10.

11.  (1)  Every kitchen sink, washbasin, bathtub and shower shall be provided, by safe equipment, with hot and cold running water.

(2)  The ordinary temperature of the hot water provided must be at least 43 degrees Celsius.  O. Reg. 21/95, s. 11.

12.  (1)  Every washroom shall be enclosed and shall have,

(a)	a water-resistant floor; and

(b)	a door that can be,

(i)	secured from the inside, and

(ii)	opened from the outside in an emergency.

(2)  Any walls and the ceiling around a bathtub or shower shall be water resistant.  O. Reg. 21/95, s. 12.

13.  No toilet or urinal shall be located in a room used for or intended to be used for sleeping or preparing, consuming or storing food.  O. Reg. 21/95, s. 13.

ELECTRICAL

14.  (1)  A supply of electrical power shall be provided to all habitable space in a residential complex.

(2)  The wiring and receptacles necessary to provide electrical power shall be maintained and shall comply with the Electrical Safety Code under the Power Corporation Act.

(3)  Every kitchen shall have outlets suitable for a refrigerator and cooking appliance.

(4)  If a rental unit has a meter for electricity for the purpose of billing the tenants of that unit, the meter shall be properly maintained and kept accessible to the tenants.  O. Reg. 21/95, s. 14.

HEATING

15.  (1)  Heat shall be provided and maintained so that the room temperature at 1.5 metres above floor level and one metre from exterior walls in all habitable space and in any area intended for normal use by tenants, including recreation rooms and laundry rooms but excluding locker rooms and garages, is at least 20 degrees Celsius.

(2)  Subsection (1) does not apply to a rental unit in which the tenant can regulate the temperature as long as a minimum temperature of 20 degrees Celsius can be maintained.

(3)  Every residential complex shall have heating equipment capable of maintaining the temperature levels required by subsection (1).

(4)  No rental unit shall be equipped with portable heating equipment as the primary source of heat.

(5)  Only heating equipment approved for use by a recognized standards testing authority shall be provided in a room used or intended for use for sleeping purposes.  O. Reg. 21/95, s. 15.

16.  (1)  Fuel supplied to a rental unit shall be supplied continuously in adequate quantities.

(2)  Utilities supplied to a rental unit shall be supplied continuously.

(3)  The supply of fuel and utilities may be interrupted for such reasonable period of time as may be required for the purpose of repair or replacement.

(4)  Subsections (1) and (2) do not apply if the tenancy agreement makes the tenant responsible for the supply of fuel or utilities and the supply has been discontinued because of arrears in payment.  O. Reg. 21/95, s. 16.

17.  Heating systems, including stoves, heating appliances, fireplaces intended for use, chimneys, fans, pumps, filtration and other equipment provided to supply heat, shall be maintained.  O. Reg. 21/95, s. 17.

18.  (1)  A space that contains heating equipment that burns fuel shall have natural or mechanical means of supplying the air required for combustion.

(2)  If heating equipment burns solid or liquid fuel, a storage place or receptacle for the fuel shall be provided in a safe place and maintained in a safe condition.  O. Reg. 21/95, s. 18.

LIGHTING AND VENTILATION

19.  (1)  All habitable space shall have artificial lighting to the level required by the Building Code.

(2)  All exterior and interior common areas shall have artificial lighting sufficient so that those areas can be used or passed through safely and this artificial lighting shall be maintained in a good state of repair.

(3)  Artificial lighting in interior common areas that meets the level required by the Building Code is sufficient for the purpose of subsection (2).  O. Reg. 21/95, s. 19.

20.  All habitable space shall have natural or mechanical means of ventilation in accordance with the Building Code.  O. Reg. 21/95, s. 20.

21.  (1)  Every bedroom, living room and dining room shall have a window (which may be part of a door) to the outside.

(2)  A window is not required in a dining room if electrical lighting is provided.

(3)  A window is not required in a living room or dining room if,

(a)	there is an opening in a dividing wall to an adjoining room;

(b)	the adjoining room has a window to the outside; and

(c)	the total window area of the room is at least 5 per cent of the combined floor areas.  O. Reg. 21/95, s. 21.

22.  (1)  This section applies with respect to every window in a rental unit that is in a storey above the storey that has,

(a)	its floor closest to ground level; and

(b)	its ceiling more than 1.8 metres above average ground level.

(2)  At the request of the tenant, each window referred to in subsection (1) shall be equipped with a safety device to prevent any part of the window from opening so as to admit a sphere greater than 100 millimetres in diameter.

(3)  No window referred to in subsection (1) shall be equipped with a safety device that makes it incapable of being opened by an adult tenant in an emergency without the use of tools.  O. Reg. 21/95, s. 22.

23.  (1)  Every existing opening in the exterior surface of a building designed for a door, window or skylight shall be equipped with a door, window or skylight capable of performing the intended function.

(2)  Doors, windows and skylights shall be maintained so that,

(a)	they are weathertight; and

(b)	any damaged or missing parts are repaired or replaced.  O. Reg. 21/95, s. 23.

24.  Chimneys, smoke-pipes, flues and gas vents shall be kept clear of obstructions and maintained so as to prevent the escape of smoke or gases into a building containing one or more rental units.  O. Reg. 21/95, s. 24.

PART IV
SAFETY AND SECURITY

25.  (1)  Every building containing a rental unit and every rental unit within it shall have a safe, continuous and unobstructed passage from every part of the interior to a safe exterior open space at street or ground level.

(2)  A secondary means of exit shall be provided if the Building Code so requires.  O. Reg. 21/95, s. 25.

26.  (1)  Every rental unit shall have an operable smoke alarm.

(2)  Every residential complex shall, if required by the Building Code or Fire Code, have operable smoke alarms installed in the locations required by the applicable Code.

(3)  The smoke alarms shall be installed with permanent connections to an electrical circuit with no disconnect switch or shall be battery operated.  O. Reg. 21/95, s. 26.

27.  Finishes, materials, storage and separations between rental units shall be in accordance with the Building Code and the Fire Code and shall be properly maintained.  O. Reg. 21/95, s. 27.

28.  All habitable space shall be separated by a fire-rated separation from any furnace or boiler.  O. Reg. 21/95, s. 28.

29.  If a guard is required by the Building Code for a newly constructed or renovated area, a guard shall be provided and maintained even though new construction or renovation is not undertaken.  O. Reg. 21/95, s. 29.

30.  (1)  A guard shall be provided and maintained along the open sides of stairs, ramps, balconies, mezzanines, landings or other areas where the vertical drop from the open side exceeds 60 centimetres.

(2)  A guard provided under subsection (1) shall provide reasonable protection from accidents for any person on the premises.  O. Reg. 21/95, s. 30.

31.  (1)  Exterior common areas shall be maintained in a condition suitable for their intended use and free of hazards and, for these purposes, the following shall be removed:

1.	Noxious weeds as defined in the regulations to the Weed Control Act and dead, decayed or damaged trees or parts of such trees that create an unsafe condition.

2.	Rubbish or debris, including abandoned motor vehicles.

3.	Structures that create an unsafe condition.

4.	Unsafe accumulations of ice and snow.

(2)  An inoperative motor vehicle or trailer that has remained in an exterior common area for more than a reasonable amount of time shall be removed.

(3)  Wells and holes in exterior common areas shall be filled or safely covered or protected.  O. Reg. 21/95, s. 31.

32.  (1)  An abandoned or inoperable icebox, refrigerator or freezer shall not be left in a common area unless it is awaiting removal.

(2)  An icebox, refrigerator or freezer that is awaiting removal shall have all its doors removed.  O. Reg. 21/95, s. 32.

33.  (1)  Driveways, ramps, parking garages, parking areas, paths, walkways and outside stairs or landings and any similar area shall be maintained to provide a safe surface for normal use.

(2)  Parking garages shall be maintained so as to prevent the accumulation of toxic fumes or the escape of toxic fumes into a building containing rental units.  O. Reg. 21/95, s. 33.

34.  (1)  Every window and exterior door, including a balcony door, that is capable of being opened and that is accessible from outside a rental unit or a building containing a rental unit shall be equipped so that it can be secured from the inside.

(2)  At least one entrance door in a rental unit shall be capable of being locked from outside the unit.

(3)  If a vestibule door locking release and the rental unit-to-vestibule communication system is provided it shall be maintained.

(4)  Parking areas that are intended to be secured, shared locker rooms and shared storage rooms shall be provided with doors equipped with security devices that prevent access to persons other than the landlord and tenants.

(5)  A mail delivery slot and other openings for deliveries that enter directly into a rental unit shall be located and maintained to prevent access to the mechanisms locking or securing any door or window.

(6)  Subsection (5) does not apply with respect to a mail delivery slot or other opening that has been sealed.

(7)  Mail boxes provided by the landlord shall be properly maintained and capable of being secured.  O. Reg. 21/95, s. 34.

PART V
MISCELLANEOUS

35.  Every floor, stair, veranda, porch, deck, balcony and loading dock, every structure similar to any of them, and any covering, guard or surface finishing shall be maintained.  O. Reg. 21/95, s. 35.

36.  Every cabinet, cupboard, shelf and counter top provided by the landlord of the rental unit shall be maintained in a structurally sound condition, free from cracks and deterioration.  O. Reg. 21/95, s. 36.

37.  (1)  Interior cladding of wall and ceilings shall be maintained free from holes, leaks, deteriorating materials, mould, mildew or other fungi.

(2)  A protective finish shall be applied to all repairs made to walls and ceilings.  O. Reg. 21/95, s. 37.

38.  Appliances supplied by the landlord of the rental unit shall be maintained in working order in a safe and efficient operating condition at all times.  O. Reg. 21/95, s. 38.

39.  Those portions of a residential complex used for human habitation, including common areas, shall be maintained to minimize heat loss through air infiltration.  O. Reg. 21/95, s. 39.

40.  Locker and storage rooms shall be kept free of dampness and mildew.  O. Reg. 21/95, s. 40.

41.  Elevators intended for use by tenants shall be properly maintained and kept in operation except for such reasonable time as may be required to repair or replace them.  O. Reg. 21/95, s. 41.

42.  All common areas shall be kept clean.  O. Reg. 21/95, s. 42.

43.  (1)  In a building containing more than one rental unit, one or more suitable containers or compactors shall be provided for garbage.

(2)  Garbage in a container or compactor provided in accordance with subsection (1) shall be stored and either placed for pick-up or regularly disposed of so as not to cause a risk to the health or safety of any person.

(3)  A container or compactor provided in accordance with subsection (1) shall be maintained in a clean and sanitary condition, shall be accessible to tenants and shall not obstruct an emergency route, driveway or walkway.  O. Reg. 21/95, s. 43.

44.  (1)  A residential complex shall be kept reasonably free of rodents, vermin and insects at all times.

(2)  The methods used for exterminating rodents and insects shall be in accordance with applicable municipal or provincial law.

(3)  Openings and holes in a building containing rental units that might permit the entry of rodents, vermin, insects or other pests shall be screened or sealed as appropriate.  O. Reg. 21/95, s. 44.

45.  Every existing interior door shall be maintained so that it is capable of performing its intended function and any damaged or missing parts shall be repaired or replaced.  O. Reg. 21/95, s. 45.

46.  In a mobile home park or a land lease community,

(a)	fire hydrants owned by the landlord shall be regularly tested and maintained, and kept free from accumulations of snow and ice;

(b)	an adequate supply of potable water and adequate water pressure, sufficient for normal household use shall be available for each home;

(c)	an adequate supply of water and adequate water pressure  shall be available for fire fighting;

(d)	roads within the park or community shall be,

(i)	kept free of holes and cleared of snow and obstructions,

(ii)	maintained to control dust, and

(iii)	kept passable;

(e)	excavations made for repairs shall be filled in and the grounds returned to their previous condition;

(f)	mailboxes and the approaches to them shall be kept free of snow and other obstructions; and

(g)	if the space between homes was three metres or more on January 14, 1989, that space shall not be reduced to less than three metres.  O. Reg. 21/95, s. 46.

47.  (1)  Sewage holding tanks in mobile home parks or land lease communities shall be emptied whenever necessary.

(2)  Sewage connections and other components of a sewage system shall be provided in a mobile home park or land lease community and shall be permanently secured to prevent discharge of sewage.  O. Reg. 21/95, s. 47.

48.  Electrical supply and connections in a mobile home park or a land lease community supplied by a landlord of a park or community shall be maintained in a good state of repair and shall be sufficiently grounded.  O. Reg. 21/95, s. 48.

49.  Omitted (revokes other Regulations).  O. Reg. 21/95, s. 49.

Schedule

AREAS WHERE MAINTENANCE STANDARDS APPLY

| Municipality / Municipalité | Type / Catégorie |
| --- | --- |
| ADELAIDE | Township / Canton |
| AIRY | Township / Canton |
| ALBERTON | Township / Canton |
| ALGOMA | Unorganized Territory / Territoire non érigé en municipalité |
| ALICE & FRASER | Township / Canton |
| AMARANTH | Township / Canton |
| AMHERST ISLAND | Township / Canton |
| ANDERDON | Township / Canton |
| ARMOUR | Township / Canton |
| ARTEMESIA | Township / Canton |
| ARTHUR | Township / Canton |
| ASHFIELD | Township / Canton |
| ASPHODEL | Township / Canton |
| ATHOL | Township / Canton |
| ATWOOD | Township / Canton |
| AUGUSTA | Township / Canton |
| BAGOT & BLYTHFIELD | Township / Canton |
| BALDWIN | Township / Canton |
| BANGOR, WICKLOW & MCCLURE | Township / Canton |
| BARRIE | Township / Canton |
| BARRIE ISLAND | Township / Canton |
| BARRY’S BAY | Village / Village |
| BEACHBURG | Village / Village |
| BECKWITH | Township / Canton |
| BEDFORD | Township / Canton |
| BELMONT & METHUEN | Township / Canton |
| BENTINCK | Township / Canton |
| BEXLEY | Township / Canton |
| BICROFT | Township / Canton |
| BIDDULPH | Township / Canton |
| BLANSHARD | Township / Canton |
| BLUE | Township / Canton |
| BONFIELD | Township / Canton |
| BRAESIDE | Village / Village |
| BRANT | Township / Canton |
| BRETHOUR | Township / Canton |
| BRIGHTON | Town / Ville |
| BRIGHTON | Township / Canton |
| BROMLEY | Township / Canton |
| BROUGHAM | Township / Canton |
| BRUCE | Township / Canton |
| BRUCE MINES | Town / Ville |
| BRUDENELL & LYNDOCH | Township / Canton |
| BURFORD | Township / Canton |
| BURK’S FALLS | Village / Village |
| BURLEIGH & ANSTRUTHER | Township / Canton |
| BURPEE | Township / Canton |
| CALVIN | Township / Canton |
| CAMBRIDGE | Township / Canton |
| CAMDEN | Township / Canton |
| CAMDEN EAST | Township / Canton |
| CARDEN | Township / Canton |
| CARDIFF | Township / Canton |
| CARDINAL | Village / Village |
| CARLING | Township / Canton |
| CARLOW | Township / Canton |
| CASIMIR, JENNINGS & APPLEBY | Township / Canton |
| CHALK RIVER | Village / Village |
| CHAMBERLAIN | Township / Canton |
| CHAPMAN | Township / Canton |
| CHAPPLE | Township / Canton |
| CHISHOLM | Township / Canton |
| CLARENCE | Township / Canton |
| COCHRANE | Unorganized Territory / Territoire non érigé en municipalité |
| COCKBURN ISLAND | Township / Canton |
| COLBORNE | Township / Canton |
| COLCHESTER NORTH | Township / Canton |
| CONMEE | Township / Canton |
| CORNWALL | Township / Canton |
| DACK | Township / Canton |
| DALTON | Township / Canton |
| DAY & BRIGHT ADDITIONAL | Township / Canton |
| DEEP RIVER | Town / Ville |
| DELHI | Township / Canton |
| DELORO | Village / Village |
| DENBIGH, ABINGER & ASHBY | Township / Canton |
| DESERONTO | Town / Ville |
| DILKE | Township / Canton |
| DOURO | Township / Canton |
| DRUMMOND | Township / Canton |
| EAST GARAFRAXA | Township / Canton |
| EAST LUTHER | Township / Canton |
| EAST WAWANOSH | Township / Canton |
| EAST WILLIAMS | Township / Canton |
| EASTNOR | Township / Canton |
| EDWARDSBURGH | Township / Canton |
| EGREMONT | Township / Canton |
| EKFRID | Township / Canton |
| ELDON | Township / Canton |
| ELLICE | Township / Canton |
| ELZEVIR & GRIMSTHORPE | Township / Canton |
| EMO | Township / Canton |
| ERAMOSA | Township / Canton |
| EUPHRASIA | Township / Canton |
| EVANTUREL | Township / Canton |
| FARADAY | Township / Canton |
| FENELON | Township / Canton |
| FINCH | Village / Village |
| FOLEY | Township / Canton |
| FRONT OF ESCOTT | Township / Canton |
| FRONT OF YONGE | Township / Canton |
| FULLARTON | Township / Canton |
| GALWAY & CAVENDISH | Township / Canton |
| GAUTHIER | Improvement District / District en voie d’organisation |
| GILLIES | Township / Canton |
| GLACKMEYER | Township / Canton |
| GLAMORGAN | Township / Canton |
| GLENELG | Township / Canton |
| GODERICH | Township / Canton |
| GORDON | Township / Canton |
| GRATTON | Township / Canton |
| GREENOCK | Township / Canton |
| GREY | Township / Canton |
| GRIFFITH & MATAWATCHAN | Township / Canton |
| HAGAR | Township / Canton |
| HAGARTY & RICHARDS | Township / Canton |
| HAGERMAN | Township / Canton |
| HALDIMAND | Township / Canton |
| HARRIS | Township / Canton |
| HAY | Township / Canton |
| HEAD, CLARA & MARIA | Township / Canton |
| HERSCHEL | Township / Canton |
| HIBBERT | Township / Canton |
| HILLIARD | Township / Canton |
| HILLIER | Township / Canton |
| HILTON | Township / Canton |
| HOPE | Township / Canton |
| HORTON | Township / Canton |
| HOWE ISLAND | Township / Canton |
| HOWLAND | Township / Canton |
| HUDSON | Township / canton |
| HUMPHREY | Township / Canton |
| HUNGERFORD | Township / Canton |
| HUNTINGDON | Township / Canton |
| HURON | Township / Canton |
| IRON BRIDGE | Village / Village |
| JOCELYN | Township / Canton |
| JOHNSON | Township / Canton |
| JOLY | Township / Canton |
| KALADAR, ANGLESEA & EFFINGHAM | Township / Canton |
| KENNEBEC | Township / Canton |
| KENORA | Unorganized Territory / Territoire non érigé en municipalité |
| KENYON | Township / Canton |
| KERNS | Township / Canton |
| KILLALOE | Village / Village |
| KINGSTON | Township / Canton |
| KITLEY | Township / Canton |
| LA VALLEE | Township / Canton |
| LANARK | Township / Canton |
| LANCASTER | Village / Village |
| LATCHFORD | Town / Ville |
| LAVANT, DALHOUSIE & NORTH SHERBROOKE | Township / Canton |
| LAXTON, DIGBY & LONGFORD | Township / Canton |
| LIMERICK | Township / Canton |
| LOCHIEL | Township / Canton |
| LOGAN | Township / Canton |
| LONDON | Township / Canton |
| LUTTERWORTH | Township / Canton |
| MACHAR | Township / Canton |
| MACHIN | Township / Canton |
| MADOC | Township / Canton |
| MAGNETAWAN | Village / Village |
| MANITOULIN | Unorganized Territory / Territoire non érigé en municipalité |
| MARIPOSA | Township / Canton |
| MARMORA & LAKE | Township / Canton |
| MASSEY | Town / Ville |
| MATACHEWAN | Improvement District / District en voie d’organisation |
| MATILDA | Township / Canton |
| MATTAWAN | Township / Canton |
| MAYO | Township / Canton |
| McCROSSON & TOVELL | Township / Canton |
| McDOUGALL | Township / Canton |
| McKELLAR | Township / Canton |
| McKILLOP | Township / Canton |
| McMURRICH | Township / Canton |
| McNAB | Township / Canton |
| MELANCTHON | Township / Canton |
| METCALFE | Township / Canton |
| MONMOUTH | Township / Canton |
| MONO | Township / Canton |
| MONTAGUE | Township / Canton |
| MONTEAGLE | Township / Canton |
| MORLEY | Township / Canton |
| MORSON | Township / Canton |
| MOSA | Township / Canton |
| MOUNTAIN | Township / Canton |
| MULMUR | Township / Canton |
| MURRAY | Township / Canton |
| NAIRN | Township / Canton |
| NEEBING | Township / Canton |
| NEWBURGH | Village / Village |
| NEWBURY | Village / Village |
| NIPISSING | Township / Canton |
| NIPISSING | Unorganized Territory / Territoire non érigé en municipalité |
| NORFOLK | Township / Canton |
| NORMANBY | Township / Canton |
| NORTH ALGONA | Township / Canton |
| NORTH BURGESS | Township / Canton |
| NORTH DUMFRIES | Township / Canton |
| NORTH EASTHOPE | Township / Canton |
| NORTH ELMSLEY | Township / Canton |
| OAKLAND | Township / Canton |
| O’CONNOR | Township / Canton |
| OLDEN | Township / Canton |
| ONONDAGA | Township / Canton |
| OPS | Township / Canton |
| ORFORD | Township / Canton |
| ORO-MEDONTE | Township / Canton |
| OSNABRUCK | Township / Canton |
| OSPREY | Township / Canton |
| OXFORD-ON-RIDEAU | Township / Canton |
| PAIPOONGE | Township / Canton |
| PAPINEAU-CAMERON | Township / Canton |
| PARRY SOUND | Unorganized Territory / Territoire non érigé en municipalité |
| PERRY | Township / Canton |
| PICKLE LAKE | Township / Canton |
| PILKINGTON | Township / Canton |
| PITTSBURGH | Township / Canton |
| PLUMMER ADDITIONAL | Township / Canton |
| PRINCE | Township / Canton |
| PROTON | Township / Canton |
| RADCLIFFE | Township / Canton |
| RAGLAN | Township / Canton |
| RAINY RIVER | Unorganized Territory / Territoire non érigé en municipalité |
| RAMARA | Township / Canton |
| RAMSAY | Township / Canton |
| RATTER & DUNNET | Township / Canton |
| RAWDON | Township / Canton |
| REAR OF YONGE & ESCOTT | Township / Canton |
| RICHMOND | Township / Canton |
| ROCHESTER | Township / Canton |
| ROCKLIFFE PARK | Village / Village |
| RUTHERFORD & GEORGE ISLAND | Township / Canton |
| RYERSON | Township / Canton |
| SANDFIELD | Township / Canton |
| SANDWICH SOUTH | Township / Canton |
| SAUGEEN | Township / Canton |
| SEBASTOPOL | Township / Canton |
| SEVERN | Township / Canton |
| SEYMOUR | Township / Canton |
| SHEFFIELD | Township / Canton |
| SHERBORNE, McCLINTOCK, LIVINGSTONE, LAWRENCE & NIGHTENGALE | Township / Canton |
| SHERWOOD, JONES & BURNS | Township / Canton |
| SHUNIAH | Township / Canton |
| SIDNEY | Township / Canton |
| SIMCOE | Town / Ville |
| SIOUX NARROWS | Township / Canton |
| SNOWDON | Township / Canton |
| SOMERVILLE | Township / Canton |
| SOPHIASBURGH | Township / Canton |
| SOUTH ALGONA | Township / Canton |
| SOUTH DORCHESTER | Township / Canton |
| SOUTH FREDERICKSBURGH | Township / Canton |
| SOUTH MARYSBURGH | Township / Canton |
| SOUTHWOLD | Township / Canton |
| SPRINGFIELD | Village / Village |
| SPRINGWATER | Township / Canton |
| ST. MARYS | Township / Canton |
| ST. VINCENT | Township / Canton |
| STRONG | Township / Canton |
| SUDBURY | Unorganized Territory / Territoire non érigé en municipalité |
| SUNDRIDGE | Village / Village |
| SYDENHAM | Township / Canton |
| TARBUTT & TARBUTT ADDITIONAL | Township / Canton |
| THE SPANISH RIVER | Township / Canton |
| THESSALON | Township / Canton |
| THOMPSON | Township / Canton |
| THORNLOE | Village / Village |
| THUNDER BAY | Unorganized Territory / Territoire non érigé en municipalité |
| TILBURY NORTH | Township / Canton |
| TIMISKAMING | Unorganized Territory / Territoire non érigé en municipalité |
| TROUT CREEK | Town / Ville |
| TUDOR & CASHEL | Township / Canton |
| TURNBERRY | Township / Canton |
| VAL RITA-HARTY | Township / Canton |
| VERULAM | Township / Canton |
| WALLACE | Township / Canton |
| WARWICK | Township / Canton |
| WELLESLEY | Township / Canton |
| WEST CARLTON | Township / Canton |
| WEST GARAFRAXA | Township / Canton |
| WEST LUTHER | Township / Canton |
| WILBERFORCE | Township / Canton |
| WILLIAMSBURGH | Township / Canton |
| WOLFE ISLAND | Township / Canton |
| WOLFORD | Township / Canton |
| WORTHINGTON | Township / Canton |
| ZONE | Township / Canton |
| ZORRA | Township / Canton |

O. Reg. 21/95, Sched.

Français

Back to top